ETCH X DATA SHEET

- PRODUCT DESCRIPTION

ETCH X is a powdered acid reducible in water and should be used in lieu of muriatic acid for etching concrete surfaces prior to the application of any cementicious or epoxy coating. ETCH X is safer to use, easier to handle, and is more cost efficient than muriatic acid. ETCH X is neutralized with potable water.

PRODUCT NAME:	ETCH X

COMMON SYNONYMS:	AMIDOSULFONIC ACID; AMIDOSULFURIC ACID; SULFAMIDIC ACID; SULPHAMIC ACID

CHEMICAL FAMILY:	INORGANIC ACIDS

FORMULA	NH2S03H

FORMULA WT.:	97.09

CAS NO.:	5329-14-6

NIOSH/RTECS NO.:	W05950000

PRODUCT USE:	Commercial Use

- MIXING REQUIREMENTS

` ETCH X can be reduced as follows:

20 to 1 = Weak Solution

15 to 1 = Mild Solution

10 to 1 = Medium Solution

5 to 1 = Strong Solution

(1 lb. ETCH X to 1 gallon water = most muriatic acid work)

- APPLICATION PROCEDURE

Pour or spray ETCH X on surface to be cleaned. If poured, spread solution with a mop, push broom, or floor cleaning machine.  To rinse for exterior applications, use a garden hose and push broom or squeegee to extract cleaner completely. For interior applications use a mop or shop vac along with plenty of water to rinse ETCH X completely.  All ETCH X must be thoroughly extracted to proceed to the next step.